## Slide 1: BOOTH MULTIPLIER
DSD-HDL
Batch : 02
M. Sai Kishore(171FA05305)
R.V.L. Karthik(171FA05329)
Tushar Chakravarthi(171FA05362)

## Slide 2: Introduction :
Booth’s multiplication algorithm is a multiplication algorithm that multiplies two signed binary numbers in two’s complement form.
The algorithm was invented by Andrew Donald Booth in 1951 while doing research on crystallography in London.
Booth multiplier is a type of digital multiplier.
Booth algorithm uses small number of additions and shift operations to do the work of multiplication.

## Slide 3
It is a powerful algorithm for signed number multiplication which treats both:
positive number.
negative numbers.
Booth algorithm is method that will reduce the number multiplicand multiples.
MULTIPLICAND : The number to be multiplied.
MULTIPLIER : The number of times that multiplicand is to be multiplied.
Booth used desk calculators that were faster at shifting than adding.

## Slide 4
A<-0,Q(-1)<-0
M<- MULTIPLICAND
Q<-MULTIPLIER
COUNT<-n
Q(0),Q(-1)
A<-A-M
A<-A+M
Arithmetic shift right:A,Q,Q(-1) COUNT<-COUNT-1
COUNT=0?
START
END
=10
=01
=11
=00
NO
YES
Booth’s algorithm
Flow chart

## Slide 5
Example of Booth’s Algorithm(7*3)
The multiplier and multiplicand are placed in the Q and M registers.

## Slide 6
Code for booth multiplier:
module booth(
input signed y,
input en,
input signed[15:0] x,
output reg signed[31:0] z,
reg[1:0]temp,
integer i,
reg E1,
reg [15:0]y1
);
always@(x,y,en)
begin
z=32'd0;
E1=1'd0;
for(i=0;i<16;i=i+1)
begin

## Slide 7
temp={x[i],E1};
y1=-y;
case(temp)
2'd2:z[31:15]=z[31:15]+y1;
2'd1:z[31:15]=z[31:15]+y;
default:begin end
endcase
z=z>>1;
z[31]=z[30];
E1=x[i];
end
if(y==16'd32)
begin
z=-z;
end
end
endmodule

## Slide 8
TEST BENCH:
module booth_tb;
//inputs
reg [15:0] y;
reg en;
reg [15:0] x;
//outputs
wire [31:0] z;
booth uut (
.y(y),
.en(en),
.x(x),
.y(y),
.z(z)
);
initial begin

## Slide 9
y=0;
en=1;
x=0;
x=16’b0000000000000101;
y=16’b0111111111111101;
end
end module
ADVANTAGES:
It handles both positive and negative multiplier uniformly.
it reduce the number of partial product extensively, so it is used in multiplier with long operands (>16 bits).
DISADVANTAGES:
The complexity of the circuit to generate a partial product bit in the Booth encoding.

## Slide 10
APPLICATIONS:
->In the field of Digital Signal Processing and graphics applications.
->used in ALU unit of computer to calculate multiplication of signed and unsigned number in
binary form.